## Slide 1: VHDL Basics
ECE 448 – FPGA and ASIC Design with VHDL 1

## Slide 5: Features of VHDL
Technology/vendor independent
Portable
Reusable

## Slide 6: VHDL Fundamentals
ECE 448 – FPGA and ASIC Design with VHDL 6

## Slide 7: Naming and Labeling (1)
VHDL is case insensitive
Example:
Names or labels databus Databus DataBus DATABUS
are all equivalent

## Slide 8: Naming and Labeling (2)
General rules of thumb (according to VHDL-87)
All names should start with an alphabet character (a-z or A-Z)
Use only alphabet characters (a-z or A-Z) digits (0-9) and underscore (_)
Do not use any punctuation or reserved characters within a name (!, ?, ., &, +, -, etc.)
Do not use two or more consecutive underscore characters ( ) within a name (e.g., Sel A is invalid)
All names and labels in a given entity and architecture must be unique

## Slide 9: Valid or invalid?
7segment_display A87372477424
Adder/Subtractor
/reset
And_or_gate AND OR NOT
Kogge-Stone-Adder Ripple&Carry_Adder
My adder

## Slide 10: Extended Identifiers
Allowed only in VHDL-93 and higher:
Enclosed in backslashes
May contain spaces and consecutive underscores
May contain punctuation and reserved characters within a name (!, ?, ., &, +, -, etc.)
VHDL keywords allowed
Case sensitive
Examples:
/rdy/ | /My design/ | /!a/
/RDY/ | /my design/ | /-a/

## Slide 11: Free Format
11
VHDL is a “free format” language
No formatting conventions, such as spacing or indentation imposed by VHDL compilers. Space and carriage return treated the same way.
Example:
if (a=b) then
or
if (a=b) then
or
if (a =
b) then
are all equivalent

## Slide 12: Comments
Comments in VHDL are indicated with a “double dash”, i.e., “--”
  Comment indicator can be placed anywhere in the line
  Any text that follows in the same line is treated as a comment
  Carriage return terminates a comment
  No method for commenting a block extending over a couple of lines
Examples:
-- main subcircuit
Data_in <= Data_bus; -- reading data from the input FIFO

## Slide 13: Comments
Explain Function of Module to Other Designers
Explanatory, Not Just Restatement of Code
Locate Close to Code Described
  Put near executable code, not just in a header

## Slide 14: Design Entity
ECE 448 – FPGA and ASIC Design with VHDL 14

## Slide 15: Example: NAND Gate
a | b | z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a
b
z

## Slide 16: Example VHDL Code
3 sections to a piece of VHDL code
File extension for a VHDL file is .vhd
Name of the file should be the same as the entity name (nand_gate.vhd) [OpenCores Coding Guidelines]
LIBRARY DECLARATION
ENTITY DECLARATION
ARCHITECTURE BODY
LIBRARY ieee;
USE ieee.std_logic_1164.all;
ENTITY nand_gate IS PORT(
a : IN STD_LOGIC; b : IN STD_LOGIC; z : OUT STD_LOGIC);
END nand_gate;
ARCHITECTURE model OF nand_gate IS BEGIN
z <= a NAND b;
END model;

## Slide 17: Tips & Hints
These rules are not enforced by all tools
but are worth following in order to increase readability and portability of your designs
Place each entity in a different file.
The name of each file should be exactly the same as the name of an entity it contains.

## Slide 18: Tips & Hints
These rules are not enforced by all tools
but are worth following in order to increase readability and portability of your designs
Place the declaration of each port, signal, constant, and variable
in a separate line

## Slide 19: STD_LOGIC Demystified
ECE 448 – FPGA and ASIC Design with VHDL 19

## Slide 20: STD_LOGIC
What is STD_LOGIC you ask?
LIBRARY ieee;
USE ieee.std_logic_1164.all;
ENTITY nand_gate IS PORT(
: IN STD_LOGIC;
: IN STD_LOGIC; z : OUT STD_LOGIC);
END nand_gate;
ARCHITECTURE dataflow OF nand_gate IS BEGIN
z <= a NAND b;
END dataflow;

## Slide 21: BIT versus STD_LOGIC
BIT type can only have a value of ‘0’ or ‘1’
STD_LOGIC can have nine values
  ’U’,’X’,‘0’,’1’,’Z’,’W’,’L’,’H’,’-’
  Useful mainly for simulation
  ‘0’,’1’, and ‘Z’ are synthesizable (your codes should contain only these three values)

## Slide 22: More on STD_LOGIC Meanings
Do not care.
Can be assigned to outputs for the case of invalid
inputs (may produce significant improvement in resource utilization after synthesis).
Must be used with great caution.
For example in VHDL, the direct comparison
'1’ = '-’
gives FALSE.
The "std_match" functions defined in the numeric_std package must be used to make this value work
as expected:
Example:
if (std_match(address, "-11---") then ...
elsif (std_match(address, "-01---") then ... else ...
end if;
'-’

## Slide 23: Modeling Wires and Buses
ECE 448 – FPGA and ASIC Design with VHDL 23

## Slide 24: Signals
SIGNAL a : STD_LOGIC;
SIGNAL b : STD_LOGIC_VECTOR(7 DOWNTO 0);
 | a | 
 | 1 wire | 
 | b | 
 | 8 bus | 

## Slide 25: Standard Logic Vectors
SIGNAL a: STD_LOGIC;
SIGNAL b: STD_LOGIC_VECTOR(3 DOWNTO 0); SIGNAL c: STD_LOGIC_VECTOR(3 DOWNTO 0); SIGNAL d: STD_LOGIC_VECTOR(15 DOWNTO 0); SIGNAL e: STD_LOGIC_VECTOR(8 DOWNTO 0);
……….
a <= ‘1’;
b <= ”0000”; c <= B”0000”;
d <= X”AF67”; e <= O”723”;
-- Binary base assumed by default
-- Binary base explicitly specified
-- Hexadecimal base
-- Octal base

## Slide 26: Vectors and Concatenation
SIGNAL SIGNAL | a: b: | STD_LOGIC_VECTOR(3 DOWNTO 0); STD_LOGIC_VECTOR(3 DOWNTO 0); | 
SIGNAL | c, | d, e: STD_LOGIC_VECTOR(7 DOWNTO | 0);
<= <= | ”0000”; ”1111”; |  |  | 
c <= | a & b; | -- | c | = ”00001111”
d <= | ‘0’ & ”0001111”; | -- | d | <= ”00001111”
e <= | ‘0’ & ‘0’ & ‘0’ & ‘1’ & ‘1’; | ‘0’ | & | ‘1’ & ‘1’ &
 |  | -- | e | <= ”00001111”

## Slide 27: VHDL Design Styles
ECE 448 – FPGA and ASIC Design with VHDL 27

## Slide 28: VHDL Design Styles
Components and interconnects
structural
VHDL Design Styles
dataflow
Concurrent statements
behavioral (sequential)
Sequential statements
Registers
State machines
Decoders
Subset most suitable for synthesis
Testbenches

## Slide 29: xor3 Example

## Slide 30: Entity xor3_gate
LIBRARY ieee;
USE ieee.std_logic_1164.all;
ENTITY xor3_gate IS PORT(
A : IN STD_LOGIC;
B : IN STD_LOGIC; C : IN STD_LOGIC;
Result : OUT STD_LOGIC
);
end xor3_gate;

## Slide 31: Dataflow Architecture (xor3_gate)
ARCHITECTURE dataflow OF xor3_gate IS SIGNAL U1_OUT: STD_LOGIC;
BEGIN
U1_OUT <= A XOR B;
Result <= U1_OUT XOR C;
END dataflow;
U1_OUT

## Slide 32: Dataflow Description
Describes how data moves through the system and the various processing steps.
  Dataflow uses series of concurrent statements to realize logic.
  Dataflow is most useful style when series of Boolean equations can represent a logic  used to implement simple combinational logic
  Dataflow code also called “concurrent” code
Concurrent statements are evaluated at the same time; thus, the order of these statements doesn’t matter
  This is not true for sequential/behavioral statements
This order…
U1_out <= A XOR B;
Result <= U1_out XOR C;
Is the same as this order…
Result <= U1_out XOR C; U1_out <= A XOR B;

## Slide 33: Structural Architecture in VHDL 93
LIBRARY ieee;
USE ieee.std_logic_1164.all;
ENTITY xor2 IS PORT(
I1 : IN STD_LOGIC;
I2 : IN STD_LOGIC; Y : OUT STD_LOGIC);
END xor2;
ARCHITECTURE dataflow OF xor2 IS BEGIN
Y <= I1 xor I2;
END dataflow;
xor2.vhd

## Slide 34: Structural Architecture in VHDL 93
ARCHITECTURE structural OF xor3_gate IS SIGNAL U1_OUT: STD_LOGIC;
BEGIN
U1: entity work.xor2(dataflow)
PORT MAP (I1 => A,
I2 => B, Y => U1
_OUT);
U2: entity work.xor2(dataflow)
PORT MAP (I1 => U1_OUT,
I2 => C,
Y => Result);
END structural;
A B C
Result
xor3_gate
I1 I2
Y
I1 I2
Y
U1_OUT
PORT NAME
LOCAL WIRE NAME

## Slide 35: Behavioral Architecture (xor3 gate)
ARCHITECTURE behavioral OF xor3 IS BEGIN
xor3_behave: PROCESS (A, B, C)
BEGIN
IF ((A XOR B XOR C) = '1') THEN
Result <= '1';
ELSE
Result <= '0';
END IF;
END PROCESS xor3_behave;
END behavioral;

## Slide 36: Behavioral Description
It accurately models what happens on the inputs and outputs of the black box (no matter what is inside and how it works).
This style uses PROCESS statements in VHDL.

## Slide 37: Arithmetic Operators in VHDL (1)
To use basic arithmetic operations involving std_logic_vectors you need to include the following library packages:
LIBRARY ieee;
USE ieee.std_logic_1164.all;
USE ieee.std_logic_unsigned.all;
or
USE ieee.std_logic_signed.all;

## Slide 38: Arithmetic Operators in VHDL (2)
You can use standard +, - operators to perform addition and subtraction:
signal A : STD_LOGIC_VECTOR(3 downto 0); signal B : STD_LOGIC_VECTOR(3 downto 0); signal C : STD_LOGIC_VECTOR(3 downto 0);
……
C <= A + B;

## Slide 39: Different ways of performing the same operation
signal count: std_logic_vector(7 downto 0);
You can use:
count <= count + “00000001”;
or
count <= count + 1;
or
count <= count + ‘1’;

## Slide 40: Different declarations for the same operator
Declarations in the package ieee.std_logic_unsigned:
function “+” ( L: std_logic_vector;
R:std_logic_vector) return std_logic_vector;
function “+” ( L: std_logic_vector;
R: integer)
return std_logic_vector;
function “+” ( L: std_logic_vector;
R:std_logic)
return std_logic_vector;

## Slide 41
Operator overloading
Operator overloading allows different argument types for a given operation (function)
The VHDL tools resolve which of these functions to select based on the types of the inputs
This selection is transparent to the user as long as the function has been defined for
the given argument types.