## Slide 1
Data Flow Modeling of Combinational Logic

## Slide 2: Register Transfer Level (RTL) Design Description
Combinational
Logic
Combinational
Logic
Registers
…
Current Topic

## Slide 3
Data-Flow VHDL
concurrent signal assignment ()
conditional concurrent signal assignment
(when-else)
selected concurrent signal assignment
(with-select-when)
Concurrent Statements

## Slide 4
Data-flow VHDL: Example
x
y
cin
s
cout

## Slide 5
Data-flow VHDL: Example (1)
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY fulladd IS
PORT ( x : IN STD_LOGIC ;
y : IN STD_LOGIC ;
cin : IN STD_LOGIC ;
s : OUT STD_LOGIC ;
cout : OUT STD_LOGIC ) ;
END fulladd ;

## Slide 6
Data-flow VHDL: Example (2)
ARCHITECTURE dataflow OF fulladd IS
BEGIN
s <= x XOR y XOR cin ;
cout <= (x AND y) OR (cin AND x) OR (cin AND y) ;
END dataflow ;
ARCHITECTURE dataflow OF fulladd IS
BEGIN
cout <= (x AND y) OR (cin AND x) OR (cin AND y) ;
s <= x XOR y XOR cin ;
END dataflow ;
equivalent to

## Slide 7: Logic Operators
Logic operators
Logic operators precedence
and or nand nor xor not xnor
not
and or nand nor xor xnor
Highest
Lowest
only in VHDL-93
or later
Notes: No order precedents

## Slide 8: No Implied Precedence
Wanted: y = ab + cd
Incorrect
y <= a and b or c and d ;
equivalent to
y <= ((a and b) or c) and d ;
equivalent to
y = (ab + c)d
Correct
y <= (a and b) or (c and d) ;
Notes: No order precedents

## Slide 9: Signal assignment statement with a closed feedback loop
A signal appears in both sides of a concurrent assignment statement
E.g., q <= ((not q) and (not en)) or (d and en);
Syntactically correct
Form a closed feedback loop
Should be avoided

## Slide 10
Data-Flow VHDL
concurrent signal assignment ()
conditional concurrent signal assignment
(when-else)
selected concurrent signal assignment
(with-select-when)
Concurrent Statements

## Slide 11: Conditional concurrent signal assignment
target_signal <= value1 when condition1 else
value2 when condition2 else
. . .
valueN-1 when conditionN-1 else
valueN;
When - Else

## Slide 12: Most often implied structure
target_signal <= value1 when condition1 else
value2 when condition2 else
. . .
valueN-1 when conditionN-1 else
valueN;
When - Else
.…
Value N
Value N-1
Condition N-1
Condition 2
Condition 1
Value 2
Value 1
Target Signal
…
0
1
0
1
0
1

## Slide 13: Example

## Slide 14: Example

## Slide 15: Signed and Unsigned Types
Behave exactly like
STD_LOGIC_VECTOR
plus, they determine whether a given vector
should be treated as a signed or unsigned number.
Require
USE ieee.numeric_std.all;

## Slide 16: Signed, Unsigned, STD_LOGIC_VECTOR
Despite their syntax, SIGNED and UNSIGNED data types are intended mainly for arithmetic operations. On the other hand, logical operations are not allowed.

## Slide 17: Operators
Relational operators
  Can be used with std_logic_vector, signed, and unsigned
Logic and relational operators precedence
= /= < <= > >=
not
= /= < <= > >=
and or nand nor xor xnor
Highest
Lowest
Notes: No order precedents

## Slide 18: Priority of logic and relational operators
compare a = bc
Incorrect
… when a = b and c else …
equivalent to
… when (a = b) and c else …
Correct
… when a = (b and c) else …
Notes: No order precedents

## Slide 19: VHDL operators

## Slide 20
Data-Flow VHDL
concurrent signal assignment ()
conditional concurrent signal assignment
(when-else)
selected concurrent signal assignment
(with-select-when)
Concurrent Statements

## Slide 21: Selected concurrent signal assignment
with choice_expression select
target_signal <= expression1 when choices_1,
expression2 when choices_2,
. . .
expressionN when choices_N;
With –Select-When

## Slide 22: Most Often Implied Structure
with choice_expression select
target_signal <= expression1 when choices_1,
expression2 when choices_2,
. . .
expressionN when choices_N;
With –Select-When
choices_1
choices_2
choices_N
expression1
target_signal
choice expression
expression2
expressionN

## Slide 23: Allowed formats of choices_k
WHEN value
WHEN value_1 | value_2 | .... | value N
WHEN OTHERS

## Slide 24: Allowed formats of choice_k - example
WITH sel SELECT
y <= a WHEN "000",
c WHEN "001" | "111",
d WHEN OTHERS;

## Slide 25: Syntax
select_expression
  Discrete type or 1-D array
  With finite possible values
choice_i
  A value of the data type
Choices must be
  mutually exclusive
  all inclusive
  others can be used as last choice_i

## Slide 26: E.g., 4-to-1 mux

## Slide 27: Question
Can “11” be used to replace others?

## Slide 28: E.g., 2-to-22 binary decoder

## Slide 29: E.g., 4-to-2 priority encoder

## Slide 30: Question
Can we use ‘-’?

## Slide 31: E.g., simple ALU

## Slide 32: Comparison
"when-else" should be used when:
there is only one condition (and thus, only one else), as in the 2-to-1 MUX
conditions are independent of each other (e.g., they test values of different signals)
conditions reflect priority (as in priority encoder); one with the highest priority need to be tested first.

## Slide 33: Comparison
"with-select-when" should be used when there is:
more than one condition
conditions are closely related to each other (e.g., represent different ranges of values of the same signal)
all conditions have the same priority (as in the 4-to-1 MUX).

## Slide 34
Behavioral Modeling of Sequential-Circuit Building Blocks

## Slide 35: VHDL Design Styles
Components and
interconnects
structural
VHDL Design
Styles
dataflow
Concurrent
statements
behavioral
Registers
Shift registers
Counters
State machines
Sequential statements
and more
if you are careful
synthesizable

## Slide 36: Processes in VHDL
Processes Describe Sequential Behavior
Processes in VHDL Are Very Powerful Statements
  Allow to define an arbitrary behavior that may be difficult to represent by a real circuit
  Not every process can be synthesized
Use Processes with Caution in the Code to Be Synthesized
Use Processes Freely in Testbenches

## Slide 37: Anatomy of a Process
[label:] PROCESS [(sensitivity list)]
[declaration part]
BEGIN
statement part
END PROCESS [label];
OPTIONAL

## Slide 38: PROCESS with a SENSITIVITY LIST
List of signals to which the process is sensitive.
Whenever there is an event on any of the signals in the sensitivity list, the process fires.
Every time the process fires, it will run in its entirety.
WAIT statements are NOT ALLOWED in a processes with SENSITIVITY LIST.
label: process (sensitivity list)
declaration part
begin
statement part
end process;

## Slide 39: Component Equivalent of a Process
All signals which appear on the left of signal assignment statement (<=) are outputs e.g. y, z
All signals which appear on the right of signal assignment statement (<=) or in logic expressions are inputs e.g. w, a, b, c
All signals which appear in the sensitivity list are inputs e.g. clk
Note that not all inputs need to be included in the sensitivity list
priority: PROCESS (clk)
BEGIN
IF w(3) = '1' THEN
y <= "11" ;
ELSIF w(2) = '1' THEN
y <= "10" ;
ELSIF w(1) = c THEN
y <= a and b;
ELSE
z <= "00" ;
END IF ;
END PROCESS ;
w
a
y
z
priority
b
c
clk

## Slide 40
Registers

## Slide 41
Clock
D
0
1
1
–
0
1
0
1
Truth table
Graphical symbol
t
1
t
2
t
3
t
4
Time
Clock
D
Q
Timing diagram
Q(t+1)
Q(t)
D latch
D
Q
Clock

## Slide 42
Clk
D


0
1
0
1
Truth table
t
1
t
2
t
3
t
4
Time
Clock
D
Q
Timing diagram
Q(t+1)
Q(t)
D flip-flop
D
Q
Clock
Graphical symbol
0
–
Q(t)
1
–

## Slide 43
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY latch IS
PORT ( D, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END latch ;
ARCHITECTURE behavioral OF latch IS
BEGIN
PROCESS ( D, Clock )
BEGIN
IF Clock = '1' THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral;
D latch
D
Q
Clock

## Slide 44
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY flipflop IS
PORT ( D, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop ;
ARCHITECTURE behavioral OF flipflop IS
BEGIN
PROCESS ( Clock )
BEGIN
IF Clock'EVENT AND Clock = '1' THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral ;
D flip-flop
D
Q
Clock

## Slide 45
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY flipflop IS
PORT ( D, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop ;
ARCHITECTURE behavioral2 OF flipflop IS
BEGIN
PROCESS ( Clock )
BEGIN
IF rising_edge(Clock) THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral2;
D flip-flop
D
Q
Clock

## Slide 46
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY flipflop_ar IS
PORT ( D, Resetn, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop_ar ;
ARCHITECTURE behavioral OF flipflop_ar IS
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
Q <= '0' ;
ELSIF rising_edge(Clock) THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral ;
D flip-flop with asynchronous reset
D
Q
Clock
Resetn

## Slide 47
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY flipflop_sr IS
PORT ( D, Resetn, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC) ;
END flipflop_sr ;
ARCHITECTURE behavioral OF flipflop_sr IS
BEGIN
PROCESS(Clock)
BEGIN
IF rising_edge(Clock) THEN
    IF Resetn = '0' THEN
    Q <= '0' ;
    ELSE
    Q <= D ;
    END IF ;
    END IF;
END PROCESS ;
END behavioral ;
D flip-flop with synchronous reset
D
Q
Clock
Resetn

## Slide 48: Asychronous vs. Synchronous
In the IF loop, asynchronous items are
  Before the rising_edge(Clock) statement
In the IF loop, synchronous items are
  After the rising_edge(Clock) statement

## Slide 49
8-bit register with asynchronous reset
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY reg8 IS
PORT ( D : IN STD_LOGIC_VECTOR(7 DOWNTO 0) ;
Resetn, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(7 DOWNTO 0) ) ;
END reg8 ;
ARCHITECTURE behavioral OF reg8 IS
BEGIN
PROCESS ( Resetn, Clock )
BEGIN
IF Resetn = '0' THEN
Q <= "00000000" ;
ELSIF rising_edge(Clock) THEN
Q <= D ;
END IF ;
END PROCESS ;
END behavioral ;`
Resetn
Clock
reg8
8
8
D
Q

## Slide 50
Use of OTHERS
OTHERS stand for any index value that has
not been previously mentioned.
Q <= “00000001” can be written as Q <= (0 => ‘1’, OTHERS => ‘0’)
Q <= “10000001” can be written as Q <= (7 => ‘1’, 0 => ‘1’, OTHERS => ‘0’)
or Q <= (7 | 0 => ‘1’, OTHERS => ‘0’)
Q <= “00011110” can be written as Q <= (4 downto 1=> ‘1’, OTHERS => ‘0’)

## Slide 51
Counters

## Slide 52
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.std_logic_unsigned.all ;
ENTITY upcount IS
PORT ( Clear, Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(1 DOWNTO 0) ) ;
END upcount ;
ARCHITECTURE behavioral OF upcount IS
SIGNAL Count : std_logic_vector(1 DOWNTO 0);
BEGIN
upcount: PROCESS ( Clock )
BEGIN
IF rising_edge(Clock) THEN
IF Clear = '1' THEN
Count <= "00" ;
ELSE
Count <= Count + 1 ;
END IF ;
END IF;
END PROCESS;
Q <= Count;
END behavioral;
2-bit up-counter with synchronous reset
Q
Clear
Clock
upcount
2

## Slide 53
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE ieee.std_logic_unsigned.all ;
ENTITY upcount_ar IS
PORT ( Clock, Resetn, Enable : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR (3 DOWNTO 0)) ;
END upcount_ar ;
4-bit up-counter with asynchronous reset (1)
Q
Enable
Clock
upcount
4
Resetn

## Slide 54
ARCHITECTURE behavioral OF upcount _ar IS
SIGNAL Count : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
BEGIN
PROCESS ( Clock, Resetn )
BEGIN
IF Resetn = '0' THEN
Count <= "0000" ;
ELSIF rising_edge(Clock) THEN
IF Enable = '1' THEN
Count <= Count + 1 ;
END IF ;
END IF ;
END PROCESS ;
Q <= Count ;
END behavioral ;
4-bit up-counter with asynchronous reset (2)
Q
Enable
Clock
upcount
4
Resetn

## Slide 55
Shift Registers

## Slide 56: Shift register
D
Q
Sin
Clock
D
Q
D
Q
D
Q
Q(3)
Q(2)
Q(1)
Q(0)
Enable

## Slide 57: Shift Register With Parallel Load
D(3)
D
Q
Clock
Enable
Sin
D(2)
D
Q
D(1)
D
Q
D(0)
D
Q
Q(0)
Q(1)
Q(2)
Q(3)
Load

## Slide 58
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY shift4 IS
PORT ( D : IN STD_LOGIC_VECTOR(3 DOWNTO 0) ;
Enable : IN STD_LOGIC ;
Load : IN STD_LOGIC ;
Sin : IN STD_LOGIC ;
Clock : IN STD_LOGIC ;
Q : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END shift4 ;
4-bit shift register with parallel load (1)
Q
Enable
Clock
shift4
4
D
Load
Sin
4

## Slide 59
ARCHITECTURE behavioral OF shift4 IS
SIGNAL Qt : STD_LOGIC_VECTOR(3 DOWNTO 0);
BEGIN
PROCESS (Clock)
BEGIN
IF rising_edge(Clock) THEN
IF Enable = ‘1’ THEN
IF Load = '1' THEN
Qt <= D ;
ELSE
Qt <= Sin & Qt(3 downto 1); END IF ;
END IF;
END IF ;
END PROCESS ;
Q <= Qt;
END behavioral ;
4-bit shift register with parallel load (2)
Q
Enable
Clock
shift4
4
D
Load
Sin
4

## Slide 60: Circuit built of medium scale components
w
0
w
3
y
1
y
0
z
w
1
w
2
w
1
En
y
3
w
0
y
2
y
1
y
0
s(0)
0
1
s(1)
0
1
r(0)
r(1)
r(2)
r(3)
r(4)
r(5)
p(0)
p(1)
p(2)
p(3)
q(1)
q(0)
ena
z(3)
z(2)
z(1)
z(0)
dec2to4
priority
t(3)
t(2)
t(1)
t(0)
regne
D
Q
Clk
Clock
Enable
En

## Slide 61: Structural description – example (1)
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY priority_resolver IS
PORT (r : IN STD_LOGIC_VECTOR(5 DOWNTO 0) ;
s : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
clk : IN STD_LOGIC;
en : IN STD_LOGIC;
t : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END priority_resolver;
ARCHITECTURE structural OF priority_resolver IS
SIGNAL p : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
SIGNAL q : STD_LOGIC_VECTOR (1 DOWNTO 0) ;
SIGNAL z : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
SIGNAL ena : STD_LOGIC ;

## Slide 62: Structural description – example (2)
BEGIN
u1: work.mux2to1(dataflow)
PORT MAP (w0 => r(0) ,
w1 => r(1),
s => s(0),
f => p(0));
p(1) <= r(2);
p(2) <= r(3);
u2: work.mux2to1(dataflow)
PORT MAP (w0 => r(4) ,
w1 => r(5),
s => s(1),
f => p(3));
u3: work.priority(dataflow)
PORT MAP (w => p,
y => q,
z => ena);

## Slide 63: Structural description – example (3)
u4: work.dec2to4 (dataflow)
PORT MAP (w => q,
En => ena,
y => z);
u5: work.regne(behavioral)
PORT MAP (D => z ,
Enable => En ,
Clock => Clk,
Q => t );
END structural;

## Slide 64: FPGA Board
Inputs: Switches and Push Buttons
Outputs: SSDs and LEDs

## Slide 65: Seven Segment Display (SSD)
Common Anode vs. Common Cathode
  Reduce number of pins
  Common anode is active low
Digit Mutliplexing:
  Each SSD has separate common anode pin
  Multiple SSDs share the same Cathode pins
    For example, the a cathode of the four SSDs are connected together to form a single output called CA (Cathode a)
  12 pins instead of 36
  Select each SSD sequentially (setting AN0=0, then AN1=0, and so on)
  Do this “fast enough” to create the illusion that all SSDs are lit constantly

## Slide 66: SSD Multiplexing
We use a 2-bit counter (00, 01, 10, 11) and a 2x4 decoder to generate the 4 SSD enables (00 => AN0 active, 01 => AN1 active, etc.).
We use the same counter bits as select lines to a 4x1 mux to “steer” the proper Ca-Cg to the enabled SSD.

## Slide 67: Clock Division (1)
The counter value should change every 1ms to 16ms (i.e. 60Hz to 1000Hz)
Clock frequency from board (MCLK) is 100 MHz
Given the following architecture:
DIVCLK[0] is 50 MHz, DIVCLK[1] is 25 MHz, and so on
All outputs have 50% duty cycle
signal DIVCLK : STD_LOGIC_VECTOR(31 DOWNTO 0) := X"00000000";
DIV_PROCESS: PROCESS(MCLK)
BEGIN
IF rising_edge (MCLK) THEN
DIVCLK <= DIVCLK + 1;
END IF;
END PROCESS;

## Slide 68: Clock Division: Arbitrary Frequency
Target Frequency is 100 Hz  Cycle Time = 0.01 second
Original Frequency is 100 MHz  Cycle Time = 0.01 µsecond
# of original cycles = 0.01 second / 0.01 µsecond = 1000000 cycles
CLK_PROCESS: PROCESS(MCLK)
BEGIN
IF RISING_EDGE(MCLK) THEN
IF(COUNTER < "11110100001000111111") THEN
COUNTER <= COUNTER + 1;
ELSE
COUNTER <= "00000000000000000000";
END IF;
END IF;
END PROCESS;
HUNDREDHZCLOCK <= '0' WHEN COUNTER < "01111010000100100000" ELSE '1';

## Slide 69: Detour Sign Example
Design a system that receives 2-bit input from switches and displays the following words on the SSDs:
  Input = “00”  SSDs <= StOP
  Input = “01”  SSDs <= LeFt
  Input = “10”  SSDs <= rIte
  Input = “11”  Nothing is displayed (SSDs are OFF)
Multiple SSDs constantly:
  Four characters in each case  2-bit counter is needed
  Clock divider is needed (100 Hz Frequency)

## Slide 70: Block Diagram of Detour Sign

## Slide 71: Detour Sign Design Components
One possible implementation:
  Clock divider Entity
  2-bit Counter Entity
  4-to-1 MUX Entity
    Choose the 1st character (S, L, r, nothing) according to input switches
    Choose the 2nd character (t, e, I, nothing) according to input switches
    Choose the 3rd character (O, F, t, nothing) according to input switches
    Choose the 4th character (P, t, e, nothing) according to input switches
  SSD Driver to determine which character and enable the correct SSD

## Slide 73: Clock Divider VHDL Code (1)
entity HUDREDHZ_CLOCK_GENERATOR_NEW is
Port ( MCLK : in STD_LOGIC;
HUNDREDHZCLOCK : out STD_LOGIC);
end HUDREDHZ_CLOCK_GENERATOR_NEW;
architecture Behavioral of HUDREDHZ_CLOCK_GENERATOR_NEW is
SIGNAL COUNTER : STD_LOGIC_VECTOR(19 DOWNTO 0) := "00000000000000000000";
begin
CLK_PROCESS: PROCESS(MCLK)
BEGIN

## Slide 74: Clock Divider VHDL Code (2)
IF(MCLK'EVENT AND MCLK = '1') THEN
IF(COUNTER < "11110100001000111111") THEN
COUNTER <= COUNTER + 1;
ELSE
COUNTER <= "00000000000000000000";
END IF;
END IF;
END PROCESS;
HUNDREDHZCLOCK <= '0' WHEN COUNTER < "01111010000100100000" ELSE '1';
end Behavioral;

## Slide 75: Two-bit Counter VHDL Code (1)
ENTITY TWO_BIT_COUNTER IS
PORT ( SW_IN : IN STD_LOGIC_VECTOR (1 DOWNTO 0);
CLK : IN STD_LOGIC;
SW_OUT : OUT STD_LOGIC_VECTOR(1 DOWNTO 0);
Q : OUT STD_LOGIC_VECTOR (1 DOWNTO 0));
END TWO_BIT_COUNTER;
ARCHITECTURE BEHAVIORAL OF TWO_BIT_COUNTER IS
SIGNAL COUNTER : STD_LOGIC_VECTOR(1 DOWNTO 0) := "00";
SIGNAL SW_REG : STD_LOGIC_VECTOR(1 DOWNTO 0) := "00";
BEGIN

## Slide 76: Two-bit Counter VHDL Code (2)
PROCESS_COUNT : PROCESS(CLK)
BEGIN
IF RISING_EDGE(CLK) THEN
COUNTER <= COUNTER + 1;
IF COUNTER = "11" THEN
SW_REG <= SW_IN;
END IF;
END IF;
END PROCESS;
SW_OUT <= SW_REG;
Q <= COUNTER;
END BEHAVIORAL;

## Slide 77: Four-to-One MUX VHDL Code (1)
ENTITY FOUR_TO_ONE_MUX IS
PORT ( I0 : IN STD_LOGIC_VECTOR (6 DOWNTO 0);
I1 : IN STD_LOGIC_VECTOR (6 DOWNTO 0);
I2 : IN STD_LOGIC_VECTOR (6 DOWNTO 0);
I3 : IN STD_LOGIC_VECTOR (6 DOWNTO 0);
SEL : IN STD_LOGIC_VECTOR (1 DOWNTO 0);
Y : OUT STD_LOGIC_VECTOR (6 DOWNTO 0));
END FOUR_TO_ONE_MUX;
ARCHITECTURE BEHAVIORAL OF FOUR_TO_ONE_MUX IS
BEGIN

## Slide 78: Four-to-One MUX VHDL Code (2)
WITH SEL SELECT Y <=
I0 WHEN "00",
I1 WHEN "01",
I2 WHEN "10",
I3 WHEN OTHERS;
END BEHAVIORAL;

## Slide 79: SSD Driver VHDL Code (1)
ENTITY SSD_DRIVER IS
PORT ( A : IN STD_LOGIC_VECTOR (6 DOWNTO 0);
B : IN STD_LOGIC_VECTOR (6 DOWNTO 0);
C : IN STD_LOGIC_VECTOR (6 DOWNTO 0);
D : IN STD_LOGIC_VECTOR (6 DOWNTO 0);
COUNTER : IN STD_LOGIC_VECTOR (1 DOWNTO 0);
SSD_DATA : OUT STD_LOGIC_VECTOR(6 DOWNTO 0);
SSD_EN : OUT STD_LOGIC_VECTOR (7 DOWNTO 0));
END SSD_DRIVER;
ARCHITECTURE BEHAVIORAL OF SSD_DRIVER IS
BEGIN

## Slide 80: SSD Driver VHDL Code (2)
WITH COUNTER SELECT SSD_DATA <=
D WHEN "00",
C WHEN "01",
B WHEN "10",
A WHEN OTHERS;
WITH COUNTER SELECT SSD_EN <=
"11110111" WHEN "00",
"11111011" WHEN "01",
"11111101" WHEN "10",
"11111110" WHEN "11",
"11111111" WHEN OTHERS;
END BEHAVIORAL;

## Slide 81: Top Design VHDL Code (1)
ENTITY DETOUR_LAB IS
PORT ( SW_IN : IN STD_LOGIC_VECTOR (1 DOWNTO 0);
MCLK : IN STD_LOGIC;
SSD_DATA : OUT STD_LOGIC_VECTOR (6 DOWNTO 0);
SSD_EN : OUT STD_LOGIC_VECTOR (7 DOWNTO 0));
END DETOUR_LAB;
ARCHITECTURE BEHAVIORAL OF DETOUR_LAB IS
SIGNAL WIRE_HUNDREDHZ_CLOCK : STD_LOGIC;
SIGNAL WIRE_SEVSEG_DATA : STD_LOGIC_VECTOR(3 DOWNTO 0);
SIGNAL WIRE_SW_OUT : STD_LOGIC_VECTOR(1 DOWNTO 0);
SIGNAL WIRE_Q : STD_LOGIC_VECTOR(1 DOWNTO 0);
SIGNAL WIRE_CHAR_1 : STD_LOGIC_VECTOR(6 DOWNTO 0);
SIGNAL WIRE_CHAR_2 : STD_LOGIC_VECTOR(6 DOWNTO 0);

## Slide 82: Top Design VHDL Code (2)
SIGNAL WIRE_CHAR_3 : STD_LOGIC_VECTOR(6 DOWNTO 0);
SIGNAL WIRE_CHAR_4 : STD_LOGIC_VECTOR(6 DOWNTO 0);
BEGIN
CLOCK_GENERATOR : ENTITY WORK.HUDREDHZ_CLOCK_GENERATOR_NEW PORT MAP(
MCLK => MCLK,
HUNDREDHZCLOCK => WIRE_HUNDREDHZ_CLOCK);
COUNTER_2 : ENTITY WORK.TWO_BIT_COUNTER PORT MAP(
SW_IN => SW_IN,
CLK => WIRE_HUNDREDHZ_CLOCK,
SW_OUT => WIRE_SW_OUT,
Q => WIRE_Q);

## Slide 83: Top Design VHDL Code (3)
MUX_CHAR_1 : ENTITY WORK.FOUR_TO_ONE_MUX PORT MAP(
I0 => "0010010", I1 => "1000111", I2 => "0101111",
I3 => "1111111", SEL => WIRE_SW_OUT, Y => WIRE_CHAR_1);
MUX_CHAR_2 : ENTITY WORK.FOUR_TO_ONE_MUX PORT MAP(
I0 => "0000111", I1 => "0000100", I2 => "1001111",
I3 => "1111111", SEL => WIRE_SW_OUT, Y => WIRE_CHAR_2);
MUX_CHAR_3 : ENTITY WORK.FOUR_TO_ONE_MUX PORT MAP(
I0 => "1000000", I1 => "0001110", I2 => "0000111",
I3 => "1111111", SEL => WIRE_SW_OUT, Y => WIRE_CHAR_3);
MUX_CHAR_4 : ENTITY WORK.FOUR_TO_ONE_MUX PORT MAP(
I0 => "0001100", I1 => "0000111", I2 => "0000100",
I3 => "1111111", SEL => WIRE_SW_OUT, Y => WIRE_CHAR_4);

## Slide 84: Top Design VHDL Code (3)
DRIVER : ENTITY WORK.SSD_DRIVER PORT MAP(
A => WIRE_CHAR_4,
B => WIRE_CHAR_3,
C => WIRE_CHAR_2,
D => WIRE_CHAR_1,
COUNTER => WIRE_Q,
SSD_DATA => SSD_DATA,
SSD_EN => SSD_EN);
END BEHAVIORAL;

## Slide 85: Test Bench VHDL Code (1)
ENTITY DETOUR_LAB_TB IS
END DETOUR_LAB_TB;
ARCHITECTURE BEHAVIORAL OF DETOUR_LAB_TB IS
SIGNAL SW_IN_TB : STD_LOGIC_VECTOR(1 DOWNTO 0) := "00";
SIGNAL MCLK_TB : STD_LOGIC := '0';
SIGNAL SSD_DATA_TB : STD_LOGIC_VECTOR(6 DOWNTO 0);
SIGNAL SSD_EN_TB : STD_LOGIC_VECTOR(7 DOWNTO 0);
BEGIN
DETOUT_LAB_U1 : ENTITY WORK.DETOUR_LAB(BEHAVIORAL) PORT MAP( SW_IN => SW_IN_TB, MCLK => MCLK_TB,
SSD_DATA => SSD_DATA_TB, SSD_EN => SSD_EN_TB);

## Slide 86: Test Bench VHDL Code (2)
CLK_PROCESS : PROCESS
BEGIN
WAIT FOR 10ns;
MCLK_TB <= NOT(MCLK_TB);
END PROCESS CLK_PROCESS;
INPUT_PROCESS : PROCESS
BEGIN
WAIT FOR 0.1sec;
SW_IN_TB <= "01";
WAIT FOR 0.1sec;
SW_IN_TB <= "10";
WAIT FOR 0.1sec;
SW_IN_TB <= "11";
WAIT FOR 0.1sec;
SW_IN_TB <= "00";
END PROCESS INPUT_PROCESS;
END BEHAVIORAL;

## Slide 87: Push Buttons as Inputs
Debouncer Circuit:
Counter time ≈ 15 ms

## Slide 88: ?